## Slide 1: The AMD gem5 APU simulator: Modeling Heterogeneous Systems in gem5
AMD Research
December 6, 2015

## Slide 2: Objectives and scope
Objectives
  Introduce the Heterogeneous System Architecture (HSA) and AMD’s GCN GPUs
  Describe the gem5-based APU simulator
Scope
  Emphasis on the GPU side of the simulator
    APU (CPU+GPU) model, not discrete GPU
  Limitations and comparison to other GPU simulators
Why are we releasing our code?
  Encourage HSA-relevant (and AMD-relevant) research
  Improve academic collaborations
    Enable intern candidates to get experience before arriving
    Enable interns to take their experience back to school
Acknowledgement
  AMD Research’s gem5 Team
Modeling an APU systems
Notes: APU simulator which tries to model the APU system
Capabilities of this simulator is the focus here
Capabilities plays a role in mapping
Acknowledge gem5 team

## Slide 3: Acknowledgements
Alex Dutu
Ali Jafri
Arka Basu
Ayse Yilmazer
Binh Pham
Blake Hechtman
Brad Beckmann
Brandon Potter
Can Hankendi
James Wang
David Hashe
Many Contributors over the past 5+ years
Kunal Korgaonkar
Lisa Hsu
Manish Arora
Marc Orr
Mario Mendez-Lojo
Mark Leather
Mark Wilkening
Martin Brown
Matt Poremba
Mike Chu
Myrto Papadopoulou
Monir Mozumder
David Roberts
Derek Hower
Dmitri Yudanov
Eric Van Tassell
Gagan Sachdev
Jason Power
Joel Hestness
Jieming Yin
John Alsop
Joe Gross
John Kalamatianos
Nagesh Lakshminarayana
Nilay Vaish
Onur Kayiran
Si Li
Sooraj Puthoor
Steve Reinhardt
Tanmay Gangwani
Tim Rogers
Tony Gutierrez
Tushar Krishna
Yatin Manerkar
Yasuko Eckert

## Slide 4: Quick Survey
How many of you are:
  Graduate students?
  Faculty members?
  Working for government research labs?
  Working for industry?
Have you written an GPU program (CUDA, OpenCLTM, other languages)?
Have you used the following simulators:
  GPGPU-Sim?
  Multi2Sim?
  gem5?
Do you know anything about HSA?

## Slide 5: Outline
Topic | Presenter | Time
Background | Brad | 8:45 – 9:05
Compilation and Simulation flow | Tony | 9:05 – 9:30
GPU Core Model | Tony | 9:30 – 10:00
Break |  | 10:00 – 10:30
Ruby Memory Contributions | Brad | 10:30 – 11:00
Demo | Tony | 11:00 – 11:20
Comparisons/Limitations/Future Work | Brad | 11:20 – 11:45
Questions | Both | 11:45 – 12:00

## Slide 6: Background
Terminology and system overview
HSA Features
  Coherent shared virtual memory
  HSAIL: HSA Intermediate Language
HSA software stack

## Slide 7: GPU terminology
GPU
Core
L1D
GPU
Core
L1D
GPU
Core
L1D
GPU
Core
L1D
GPU I-Cache
L2
CU
TCP
CU
TCP
CU
TCP
CU
TCP
SQC
TCC
CU: Compute Unit (SM in Nvidia terminology), TCP: Texture Cache per Pipe,
TCC: Texture Cache per Channel, SQC: Sequencer Cache
AMD terminology
Notes: Clarifying AMD GPU terminology and what we use in these slides

## Slide 8: Example APU system
GPU + CPU core-Pair with a shared directory
GPU
Core
L1D
GPU
Core
L1D
GPU
Core
L1D
GPU
Core
L1D
Sequencer Cache (SQC)
L2
CPU0
CPU1
CPU I-Cache
L1D
L1D
L2
Directory
Memory
Controller
Memory
GPU
CPU
Notes: Example of a APU system.
Notice the shared/private caches and the single directory structure

## Slide 9: Traditional discrete gpu
Separate memory
Separate addr space
  No pointer-based data structures
Explicit data copying
  High latency
  Low bandwidth
Need lots of compute on GPU to amortize copy overhead
Very limited GPU memory capacity
GPU Memory
CU
1
…
CU
2
CU
3
CU
M
Coherent System Memory
CPU
1
CPU
N
…
CPU
2
PCIe™

## Slide 10: hUMA unified memory
Unified address space
  GPU uses user virtual addrs
  Fully coherent
No explicit copying
  Data move on demand
Pointer-based data structures shared across CPU & GPU
Pageable virtual addresses
  No GPU capacity constraints
Unified Coherent Memory
CPU
1
CPU
N
…
CPU
2
CU
1
…
CU
2
CU
3
CU
M

## Slide 11: HSAIL: The HSA Intermediate language
A portable virtual ISA for vendor-independent compilation and distribution
  Like Java bytecode for GPUs, similar to Nvidia PTX
Generated by a language-specific compiler (LLVM, GCC, Javac, etc.)
  Application binaries may ship with embedded HSAIL (text) or BRIG (binary)
Low-level IR, close to machine ISA level
  Most optimizations (including register allocation) performed before HSAIL
Compiled down to target ISA by a vendor-specific finalizer
  Finalizer may execute at run time, install time, or build time

## Slide 12: Programming Languages proliferating on HSA
HSAIL
Kernel Fusion Driver (KFD)
HSA Core Runtime
HSA Finalizer
HSA Helper Libraries
OpenCL™ App
OpenCL Runtime
Java App
Python
App
Continuum’s
Numba
Compiler
C++ App
HCC: C++ for Heterogeneous
Computing
Java JVM (Sumatra)
High-level compilers target HSA specification
  Examples: Shared virtual memory, scoped synchronization
Runtime infrastructure provides necessary software support to meet specification
  Examples: Address translation
  Works in concert with GPU hardware
The HSA hardware specifications are publicly available
  http://hsafoundation.com
The HSA software stack is open sourced
  http://github.com/HSAFoundation
Notes: Common infrastructure of HSAIL and HSA Runtime -> Bring benefits of GPU computing to programming languages that programmers are already using.

## Slide 13: HSA Building Blocks
HSA Hardware Building Blocks
Shared Virtual Memory
  Single address space
  Coherent
  Pageable
  Fast access from all components
  Can share pointers
Architected User-Level Queues
Signals
Context Switching
Platform Atomics
Defined Memory Model
HSA Software Building Blocks
HSAIL
  Portable, parallel, compiler IR
  Instruction definition
HSA Runtime
  Create queues
  Allocate memory
  Device discovery
Multiple high level compilers
  CLANG/LLVM/HSAIL
  C++, OpenMP, OpenACC, Python, OpenCL™, etc
Industry standard compiler IR and runtime to enable existing programming languages to target the GPU
HSA Platform System Arch Specification
Industry standard, architected requirements for how devices share memory and communicate with each other
HSA Programmer’s Reference Manual
HSA System Runtime Specification
Open-Source
Open-Source
Open-Source
http://hsafoundation.com
http://github.com/HSAFoundation
Open-Source

## Slide 14: APU Simulation Support
HSA Hardware Building Blocks
Shared Virtual Memory
  Single address space
  Coherent
  Pageable
  Fast access from all components
  Can share pointers
Architected User-Level Queues
Signals
Context Switching
Platform Atomics
Defined Memory Model
  Basic Acquire and Release operations
  No SC data
  Coarse-grain memory
HSA Software Building Blocks
HSAIL
  Portable, parallel, compiler IR
  Instruction definition
HSA Runtime (OpenCLTM Runtime)
  Create queues
  Allocate memory
  Device discovery
Multiple high-level compilers
  CLANG/LLVM/HSAIL
  C++, OpenMP, OpenACC, Python, OpenCL™, etc
Legend
Included in first release
Work-in-progress / may be released
Longer term work

## Slide 15: Hsa Terminology in a nutshell
HSA Programming Abstraction
  Light abstractions of parallel physical hardware
  Captures basic OpenCL constructs and much more
NDRange: N-Dimensional (N = 1, 2, or 3) index space
  Partitioned into workgroups, wavefronts, and work-items
GPU “Core”
GPU “Core”
GPU
GPU Architecture
Workgroup
Workgroup
NDRange
HSA Model
Wavefront
Work-item
Thread in CUDA
Grid in CUDA
Thread block in CUDA
Warp in CUDA
Notes: Lightweight abstractions to physical hardware
Similar to OpenCL and much more
Division into workgroups, wavefronts and work-items

## Slide 16: Outline
Topic | Presenter | Time
Background | Brad | 8:45 – 9:05
Compilation and Simulation flow | Tony | 9:05 – 9:30
GPU Core Model | Tony | 9:30 – 10:00
Break |  | 10:00 – 10:30
Ruby Memory Contributions | Brad | 10:30 – 11:00
Demo | Tony | 11:00 – 11:20
Comparisons/Limitations/Future Work | Brad | 11:20 – 11:45
Questions | Both | 11:45 – 12:00

## Slide 17: Overview of gem5
Open-source modular platform for system architecture research
  Integration of M5 (Univ. of Michigan) and GEMS (Univ. of Wisconsin)
  Actively used in academia and industry
Discrete-event simulation platform with numerous models
  CPU models at various performance/accuracy trade-off points
    Multiple ISAs: x86, ARM, Alpha, Power, SPARC, MIPS
  Two memory system models: Ruby and “classic” (M5)
    Including caches, DRAM controllers, interconnect, coherence protocols, etc.
  I/O devices: disk, Ethernet, video, etc.
  Full system or app-only (system-call emulation)
Cycle-level modeling (not “cycle accurate”)
  Accurate enough to capture first-order performance effects
  Flexible enough to allow prototyping new ideas reasonably quickly
See http://www.gem5.org

## Slide 18: High-level compilation FLOW
APU extensions
CPU handles x86 host binary
HSA 1.0F OpenCL compilation flow generates kernels
  CL Offline Compiler (CLOC)
  ‘F’ stands for final
  Combination of 4 different tools
  Available on GitHub
System call emulation simulation
  No OS or device driver
  Execution-driven evaluation
    GPU microarchitecture model directly executes HSAIL instructions
HSA 1.0F OpenCL Compilation Flow
x86 host binary
GPU kernel binary objects
Emulated
OpenCL, OS, driver ops.
HSAIL BRIG loader
GCC
Benchmarks

## Slide 19: HSA 1.0F Compilation flow
Example makefile commands
# Step 1: frontend CL compiler converts CL to LLVM bytecode
clc2 --enable-hsail-extensions --cl-std=CL2.0 my_kernel.cl -o my_kernel.fe.bc
# Step 2: link HSAIL builtins (available with compiler) with bytecode
llvm-link my_kernel.fe.bc –l builtins-hsail.bc –o my_kernel.linked.bc
# Step 3: optimize bytecode for GPU
opt -O3 -gpu -whole -verify my_kernel.linked.bc -o my_kernel.opt.bc
# Step 4: compile optimized bytecode to HSAIL
llc -filetype=obj -hsail-enable-gcn=0 -march=hsail-64 my_kernel.opt.bc -o my_kernel.asm
# Step 5 (optional): disassemble BRIG-HSAIL binary into human readable disassembly
hsailasm -disassemble my_kernel.asm -o my_kernel.dasm
CL compiler
LLVM Linker
Optimizer
Low-level Compiler
CL Kernels
HSAIL-builtins
BRIG HSAIL binary
Compiler toolchain available at:
https://github.com/HSAFoundation/CLOC
HSA 1.0F OpenCL Compilation Flow

## Slide 20: Emulated Cl Runtime
Our implementation of OpenCL 2.0 runtime API
  Simplifies OpenCL runtime for use with simulator
  No OS kernel driver in SE mode, all driver calls captured by emulated driver
    open()
      Standard Unix system call for opening a device
      Returns file descriptor for open device
    ioctl()
      (I/O control) standard Unix system call for sending commands to a device
      Sends device-specific request codes, which are provided by the driver
  Emulates kernel launch API, memory allocation, etc.
  Maintains in-memory HSA tasks and launch “doorbell” – visible to GPU HW
  HSAIL is directly executed, no need to build/compile kernel through OpenCL
Available at: http://gem5.org/GPU_Models

## Slide 21: High-Level APU Simulation FLOW
GPU kernel binary objects
GPU kernel binary objects
AMD added components
  Supports simultaneous execution of multiple kernels
Details
  GCN GPU model
  Flexible memory system
CPU-GPU Communication
  via coherent shared virtual memory
Application Execution
Ruby
X86 CPU
X86 CPU
X86 CPU
X86 CPU
X86 CPU
X86 CPU
X86 CPU
CU
CPU
GPU Cache
Hierarchy
HSAIL BRIG loader
Emulated
OpenCL, OS, driver ops.
x86 host binary
GPU kernels

## Slide 22: Detailed view of Kernel launch
gem5
Application
Emulated OpenCL runtime
Emulated Driver
open()/ioctl()
HsaQueueEntry Addr A
Doorbell Addr B
Simulated Mem.
Run on simulated CPU
CUs
Dispatcher
BRIG Loader
kernels.asm (BRIG HSAIL kernel binary)
Shader
HSA Kernels
clEnqueueNDRangeKernel()
Decoder
Instructions are pre-decoded…
… then stored in kernel object
memcpy(HsaQueueEntry, KernelObject);
*Doorbell = 0; // MEM[Addr B] = 0;
write(Addr B);
Launch kernel

## Slide 23: Detailed View of kernel launch
GPU Dispatcher
// Doorbell mapped to GPU I/O space
volatile uint32_t *dispatcherDoorbell = (uint32_t*)0x10000000;
// Task mapped to GPU I/O space
HsaQueueEntry *hsaTaskPtr = (HsaQueueEntry*)0x10000008;
clEnqueueNDRangeKernel()
{ …
/* Reads/writes to these data stuctures will trigger
I/O reads/writes to dispatcher. Copies newly
created kernel to GPU. */
memcpy(hsaTaskPtr, &curHsaTask, sizeof(HsaQueueEntry));
// Notify dispatcher that kernel copy is finished;
// launch kernel.
*dispatchDoorbell = 0;
return CL_SUCCESS;
}
Dispatcher I/O space mapped to 0x10000000 – 0x10000FFF
Copy HSA task to Dispatcher
curTask
NDRange
NDRange
-
-
NDRangeMap
0
1
2
3
Create and store a new NDRange
NDRange
ID
Schedule workgroup dispatch

## Slide 24: Dispatcher workgroup assignment
1) Try to dispatch queued WGs on every tick
2) Pick oldest NDRange in queue; if it has unexecuted WGs, try to schedule them on a CU
3) Dispatch WG to CU if there are enough WF slots, enough VGPRs, and enough LDS space.
Shader
CU
CU
CU
GPU Dispatcher
curTask
NDRange
NDRange
-
NDRangeMap
0
1
2
3
ID
-
NDRange
NDRange
wg(0, 0, 0)
wg(1, 0, 0)
wg(0, 1, 0)
wg(1, 1, 0)
work-item

## Slide 25: Outline
Topic | Presenter | Time
Background | Brad | 8:45 – 9:05
Compilation and Simulation flow | Tony | 9:05 – 9:30
GPU Core Model | Tony | 9:30 – 10:00
Break |  | 10:00 – 10:30
Ruby Memory Contributions | Brad | 10:30 – 11:00
Demo | Tony | 11:00 – 11:20
Comparisons/Limitations/Future Work | Brad | 11:20 – 11:45
Questions | Both | 11:45 – 12:00

## Slide 26: GPU Core BASED on GCN ARCHITECTURE
GPU core in the APU simulator modeled after Graphics Core Next (GCN) Architecture
  More details available here: GCN Architecture Whitepaper www.amd.com/Documents/GCN_Architecture_whitepaper.pdf
fetch_unit.hh/cc
fetch_stage.hh/cc
wavefront.hh/cc
vector_register_file.hh/cc
vector_register_state.hh/cc
lds_state.hh/cc
local_memory_pipeline.hh/cc
global_memory_pipeline.hh/cc
brig_object.hh/cc
hsail_code.hh/cc
arch/hsail/decoder.hh
arch/hsail/decoder.cc (auto-generated)
gpu_static_inst.hh/cc
auto-generated ISA-specific instruction classes
compute_unit.hh/cc
shader.hh/cc
Notes: One comment is keep names consistent

## Slide 27: GPU CORE MODULES
GPU CORE MODULES vs. RUBY MODULES
GPU Core
L1D
GPU Core
L1D
GPU Core
L1D
GPU Core
L1D
SQC (I-Cache)
L2
Hardware building blocks
GPU (shader unit) contains multiple CUs
GPU core is the compute unit (compute_unit.[cc|hh])
  Resources inside GPU Core
    Instruction buffering, Registers, Vector ALUs
  Resources outside GPU Core
    TCP, TCC, I-Cache (Ruby based)
Shader (shader.[cc|hh]): Object containing all GPU cores along with other misc. components
GPU Core
Modules
APU
Simulator
Ruby
Modules
Simulator software modules

## Slide 28: GPU CORe MODULE INTERNALS
Compute unit (CU)
  Four 16-wide SIMD units for vector processing
  SIMD hosts wavefronts (WF)
  Private resources to each SIMD
    Instruction buffering
    Registers
    Vector ALUS
  Shared resources
    Fetch and decode
    TCP (L1D)
    Local data share (LDS)
      Similar to Nvidia shared memory
SHARED vs. PRIVATE STRUCTURES
GPU Core
L1D
GPU Core
L1D
GPU Core
L1D
GPU Core
L1D
SQC (I-Cache)
L2
Instruction Fetch
WF 0-9 Contexts
WF 10-19 Contexts
WF 20-29 Contexts
WF 30-39 Contexts
Instruction Decode
SIMD 0
Vector Registers
Vector ALU
SIMD 1
Vector Registers
Vector ALU
SIMD 2
Vector Registers
Vector ALU
SIMD 3
Vector Registers
Vector ALU
TCP (L1D)
Local Data Share (LDS)

## Slide 29: GPU Core TIMING
Functional and timing code separation
  Wherever applicable, and similar to gem5
  Global memory operation timings handled by Ruby model
    Timing schedule accesses with some delay and delay responses
    Functional will complete instruction in a single cycle
Progressively detailed component models
  Examples: register file, TLB operations, etc.
Register file
  Simple register allocation model available
  Different register organizations and access arbitration policies possible using its API
Design Methodology
Functional
Timing
More detailed
Less Detailed
Notes: Give an example for GPU register. May be some some common interface.

## Slide 30: GPU CORE Timing
Fetch
Scoreboard
Execute
Schedule
Memory pipeline
Execute-in-execute philosophy
Pipeline stages
  Fetch: fetch for dispatched wavefronts - fetch_stage.[hh|cc]
  Scoreboard: Check which wavefronts are ready - scoreboard_check_stage.[hh|cc]
  Schedule: Select a wave from the ready pool - schedule_stage.[hh|cc]
  Execute: Run WF on execution resource - exec_stage.[hh|cc]
  Memory pipeline: Execute lds/global memory operation
    local_memory_pipeline.[hh|cc]
    global_memory_pipeline.[hh|cc]
Instructions are decoded when the kernels are loaded
CONCEPTUAL TIMING STAGES
Fetched WFs
Ready WFs
Executing WFs
local memory (LDS)
global memory (TCP)
Notes: These are not pipeline stages
If not in a pipeline fashion then how are we keeping track of timing
Is the cost of moving between queues zero (how is this implemented in hardware)
Capability vs. accuracy tradeoff

## Slide 31: Fetch and Wavefront contexts
SQC shared by 4 CUs (GPU_RfO-SQ.sm, GPU_VIPER-SQC.sm)
  # of SQCs and CUs are configurable in simulator
Fetch (fetch_unit.[hh|cc], fetch_stage.[hh|cc])
  Shared and arbitrated between SIMDs in a CU
  Fetch to each SIMD unit
  Don’t fetch if instruction buffer (IB) contains branch
WF Contexts (wavefront.[hh|cc])
  10 WFs per SIMD, 40 per CU
    PC and instruction buffers
    Reconvergence stack (for branch divergence)
      Used to determine reconvergence point for work items that experience branch divergence – typically immediate post-dominator
Instruction Fetch
WF 0-9
Contexts
WF 10-19
Contexts
WF 20-29
Contexts
WF 30-39
Contexts
Instruction Decode
SIMD 0
Vector Registers
Vector ALU
SIMD 1
Vector Registers
Vector ALU
SIMD 2
Vector Registers
Vector ALU
SIMD 3
Vector Registers
Vector ALU
Local Data Share (LDS)
TCP (L1D)
4-CU-shared SQC (I-Cache)
PC
IB
Wavefront 0
PC
IB
Wavefront 1
PC
IB
Wavefront 9
SIMD Phase
BB1
BB1
BB1
BB1
if
else
reconvergence point

## Slide 32: Decode and issue
Decode and issue
  All instructions pre-decoded by loader and cached by PC
  After fetching an instruction it is retrieved from decode cache
  Decode and issue N instructions from the SIMD’s 10 WFs
  Instruction types supported:
    Branch, vector ALU, vector memory, local data share, export, and special instructions
  Issuing restrictions:
    Only one instruction type at a time per SIMD
    Each instruction from a different WF
PC
IB
Wavefront 0
PC
IB
Wavefront 1
PC
IB
Wavefront 9
SIMD Phase
Instruction Fetch
WF 0-9
Contexts
WF 10-19
Contexts
WF 20-29
Contexts
WF 30-39
Contexts
Instruction Decode
SIMD 0
Vector Registers
Vector ALU
SIMD 1
Vector Registers
Vector ALU
SIMD 2
Vector Registers
Vector ALU
SIMD 3
Vector Registers
Vector ALU
Local Data Share (LDS)
TCP (L1D)

## Slide 33: Vector Register file
Vector General Purpose Registers (vGPRs)
  Partitioned into 4 independent slices, 1 per SIMD
    Configurable size
  Why? Because each SIMD executes independent WF
  32-bit wide
  Combine adjacent vGPRs for 64-bit or 128-bit data
  Each WF also has a set of 32-bit (SReg), 64-bit (DReg), and 1-bit predicate (CReg)
Register Allocation Done by a Simple Pool Manager
  Modular design – more advance pool managers can be swapped into VRF seamlessly
  Simple timing model with constant delay
Instruction Fetch
SIMD 0
Phases
SIMD 1
Phases
SIMD 2
Phases
SIMD 3
Phases
Instruction Decode
SIMD 0
Vector Registers
Vector ALU
SIMD 1
Vector Registers
Vector ALU
SIMD 2
Vector Registers
Vector ALU
SIMD 3
Vector Registers
Vector ALU
Local Data Share (LDS)
TCP (L1D)
vGPRs

## Slide 34: Vector ALUs
16-lane vector pipeline per SIMD
  Each lane has a set of functional units
  One work-item per lane
4 cycles to execute a WF for all 64 work-items (in the best case)
  In gem5, 64 work-items are executed in one tick and ticks are multiplied by 4
SIMD execution may take longer if work-items in WF have dissimilar behaviors
  Example 1: Branch (or spatial) divergence
    Branches executed through predication
    When control flow diverges, all lanes take all paths
      4 cycles for one path and another 4 cycles for the other
  Example 2: Memory (or temporal) divergence
    Longer access latency by one work-item stalls entire WF
Instruction Fetch
WF 0-9
Contexts
WF 10-19
Contexts
WF 20-29
Contexts
WF 30-39
Contexts
Instruction Decode
SIMD 0
Vector Registers
Vector ALU
SIMD 1
Vector Registers
Vector ALU
SIMD 2
Vector Registers
Vector ALU
SIMD 3
Vector Registers
Vector ALU
Local Data Share (LDS)
TCP (L1D)
Vector ALU in SIMD
Lane 0
Lane 1
Lane 15

## Slide 35: GPU CORE TIMING
Memory instructions are handled through memory transactions
  Part of GPU core modules (gpu_dyn_inst.[cc|hh])
Memory instruction handled in multiple phases
  Appropriate instruction specific execute() methods per instruction per ISA
New machine ISAs can use this capability to support its own memory instructions
Individual stages contribute to the memory instruction timing
  Additionally memory end timing handled by ruby and memory technology parameters
  global_memory_pipeline.[hh|cc] and local_memory_pipline.[hh.cc]
Handling Memory INSTRUCTIONS
GPU dynamic memory instruction
Create packet
Global/LDS operation
Write back

## Slide 36: Vector memory execution
In gem5:
  Address calculation: arch/hsail/inst/mem_impl.hh
  Address coalescing mem/ruby/system/GPUCoalescer.[hh|cc]
  TCP in mem/protocol/GPU_RfO-TCP.sm, GPU_VIPER-TCP.sm
  TCC in mem/protocol/GPU_RfO-TCC.sm, GPU_VIPER-TCC.sm
Instruction Fetch
WF 0-9
Contexts
WF 10-19
Contexts
WF 20-29
Contexts
WF 30-39
Contexts
Instruction Decode
SIMD 0
Vector Registers
Vector ALU
SIMD 1
Vector Registers
Vector ALU
SIMD 2
Vector Registers
Vector ALU
SIMD 3
Vector Registers
Vector ALU
Local Data Share (LDS)
TCP (L1D)
4-CU-shared TCC (L2)
Coalesce
Tag
Decompression
Data
TCP
Address
Write data
Read data
To shared TCC (L2)
Local Data Store (LDS) – (lds_state.[hh|cc])
  User-managed address space
  Scratchpad for WFs in workgroup
  Used for data sharing and synchronization within workgroup
  Cleared when workgroup completes
  In gem5, functional model with a pointer per workgroup

## Slide 37: HSAIL ISA Support
Decouple GPU microarchitecture model from ISA specification
Currently supports HSAIL
  Others could easily be added
Architecture description files
  Instructions are generated similar to gem5 CPU ISAs
  Appropriate class hierarchies (e.g., as in HSAIL)
Interfaces with the GPU core modules
  Execute methods are instruction specific
  Standard set of APIs via instruction wrapper (GPUStaticInst class)
  Wavefront exposes the APIs to instructions
GPU core model components
ISA-specific instruction classes and methods
WF-related interfaces
Static instruction objects with no dynamic information
Instruction and ISA specific classes
Dynamic instruction information and interfaces
Notes: Explain gpustaticinst
Explain why the wavefront interface is important

## Slide 38: Isa description/microarchitecture separation
GPU core model components
ISA specific instruction classes and methods
Wavefront related interfaces
Static instruction objects with no dynamic information
Instruction and ISA specific classes
Dynamic instruction information and interfaces
GPUStaticInst & GPUDynInst (gpu_static_inst.[hh|cc] gpu_dyn_inst.[hh|cc])
  Architecture-specific code src/gpu/arch/
  Base instruction classes
  Define API for instruction execution
    E.g., execute() – perform instruction execution
  Implemented by ISA-specific instruction classes e.g., HsailGPUStaticInst (arch/hsail/insts/gpu_static_inst.[hh|cc])
GPUExecContext gpu_exec_context.[hh|cc]
  Define API for accessing ISA state
Shader
Compute Units
Wavefronts
HSAIL Static Inst
HSAIL Code
HSAIL Decoder
Operands
ISA State
GPUStaticInst
GPUDynInst
GPUExecContext
HSACode
GPU core state [src/gpu]
ISA-specific state [src/gpu/arch]
GPU Core/ISA API
definition [src/gpu]
Notes: Explain gpustaticinst
Explain why the wavefront interface is important

## Slide 39: Pseudo-Instruction
Magic instructions for GPU kernels: researcher-defined functionality
  Explore new hardware mechanisms
  Profile and trace
  Debug simulated kernels
  Uses HSAIL Call instruction
    Calls function based on signature
    Prefix function with “__gem5_hsail_op”
    Call::execute() checks for “__gem5_hsail_op” in function name, calls appropriate pseudo op
Examples include
  HSAIL instructions not exposed in high-level languages (e.g., cross-lane instructions)
  Print statements and panic instruction within the GPU kernel
  GDB break points
Source files
  [gem5] src/gpu/arch/hsail/insts/decl.hh
  [gem5] src/gpu/arch/hsail/insts/pseudo_inst.cc

## Slide 40: Outline
Topic | Presenter | Time
Background | Brad | 8:45 – 9:05
Compilation and Simulation flow | Tony | 9:05 – 9:30
GPU Core Model | Tony | 9:30 – 10:00
Break |  | 10:00 – 10:30
Ruby Memory Contributions | Brad | 10:30 – 11:00
Demo | Tony | 11:00 – 11:20
Comparisons/Limitations/Future Work | Brad | 11:20 – 11:45
Questions | Both | 11:45 – 12:00

## Slide 41: Outline
Topic | Presenter | Time
Background | Brad | 8:45 – 9:05
Compilation and Simulation flow | Tony | 9:05 – 9:30
GPU Core Model | Tony | 9:30 – 10:00
Break |  | 10:00 – 10:30
Ruby Memory Contributions | Brad | 10:30 – 11:00
Demo | Tony | 11:00 – 11:20
Comparisons/Limitations/Future Work | Brad | 11:20 – 11:45
Questions | Both | 11:45 – 12:00

## Slide 42: Ruby background
Flexible Memory System
  Rich configuration
    Simulate combination of caches, coherence, interconnect, etc…
  Rapid prototyping
    Domain-Specific Language (SLICC) for coherence protocols
    Modular components
Detailed statistics
  Latency distributions for requests
  Generated state transitions, network utilization, etc.
Detailed component simulation
  Network (fixed/flexible Garnet pipelines and simple)
  Caches (pluggable replacement policies)
  Memory (shared memory controllers between Classic and Ruby)

## Slide 43: Synchronization Background
Traditional synchronization
  Kernel Begin: All stores from CPU and prior kernel completions are visible.
  Kernel End: All stores from a kernel are visible to CPU and future kernels.
  Barrier: All members of a workgroup are at the same PC and all prior stores in program order will be visible.
HSA specification includes Load-Acquire and Store-Release
  Load-Acquire (LdAcq): A load that occurs before all memory operations later in program order (like Kernel Begin).
  Store-Release (StRel): A store that occurs after all prior memory operations in program order (like Kernel End or Barrier).
Notes: Prepare for questions on HSA semantics (CPU reading data).

## Slide 44: APU Contributions To Ruby/SLICC
4 APU SLICC protocols
  1 GPU Read-for-Ownership (RFO) protocol
    Used by Hechtman et al. [HPCA 2014] and Orr et al. [ISCA 2014]
  3 GPU Write-Through protocols – called VIPER
    Used by Hechtman et al. [HPCA 2014] and Power et al. [MICRO 2013]
  All 4 protocols use the same CPU cache controllers
    Core-Pair design with write-through L1 caches (separate L1 D, shared L1 I & L2)
  Also includes 1 CPU-only protocol: MOESI_AMD_Base
  Support single coherent address space and copies between emulated address spaces
Request coalescing
Hierarchical network topology configuration

## Slide 45: GPU RFO coherence
Read-for-ownership coherence, Sequential consistency
Maintains the single writer / multiple reader invariant per cache block
  Typical for existing CPU protocols
  Non-typical for GPUs, but provides good comparison
Wavefront coalescing of writes at the CU
LdAcq, StRel are simply Ld and St operations
Invalidations, dirty-writeback and data responses
Tested using the ruby random tester
Uses an inclusive directory at the TCC
Notes: Image from https://openclipart.org/detail/28107/processoridle
License: https://openclipart.org/unlimited-commercial-use-clipart

## Slide 46: GPU RFO protocol
GPU
Core
L1D
GPU
Core
L1D
GPU
Core
L1D
GPU
Core
L1D
L1I (SQC)
L2
CPU0
CPU1
CPU I-Cache
L1D
L1D
L2
Directory
Memory
Controller
Memory
GPU
CPU
L2 directory
MOESI_AMD_Base-dir.sm
GPU_RfO-SQC.sm
GPU_RfO-TCP.sm
GPU_RfO-TCC.sm
GPU_RfO-TCCdir.sm
MOESI_AMD_Base-CorePair.sm
Notes: Example of a APU system.
Notice the shared/private caches and the single directory structure

## Slide 47: GPU Viper coherence protocols
Write-through coherence, Release consistency
GPU write-through protocols
  Writes performed immediately
  No stalling for exclusive permissions
  Maintains per-byte dirty masks
LdAcq -> invalidate entire L1 cache
StRel -> ensure prior write-throughs complete
Minimal data verification testing
  A great opportunity for research
Uses the same CPU core-pair cache controller as GPU_RfO
3 variants with different directory implementations
  GPU_VIPER: Stateless Directory
  GPU_VIPER_Baseline: Probe Filter Directory
  GPU_VIPER_Region: Region Directory
Notes: Image from https://openclipart.org/detail/99781/snake
License: https://openclipart.org/unlimited-commercial-use-clipart

## Slide 48: GPU VIPER protocol
GPU
Core
L1D
GPU
Core
L1D
GPU
Core
L1D
GPU
Core
L1D
L1I (SQC)
L2
CPU0
CPU1
L1I
L1D
L1D
L2
Stateless
Directory
Memory
Controller
Memory
GPU
CPU
MOESI_AMD_Base-dir.sm
GPU_VIPER-SQC.sm
GPU_VIPER-TCP.sm
GPU_VIPER-TCC.sm
MOESI_AMD_Base-CorePair.sm
Notes: Example of a APU system.
Notice the shared/private caches and the single directory structure

## Slide 49: GPU VIPER Baseline protocol
GPU
Core
L1D
GPU
Core
L1D
GPU
Core
L1D
GPU
Core
L1D
L1I (SQC)
L2
CPU0
CPU1
L1I
L1D
L1D
L2
Probe
Filter
Memory
Controller
Memory
GPU
CPU
MOESI_AMD_Base-probeFilter.sm
GPU_VIPER-SQC.sm
GPU_VIPER-TCP.sm
GPU_VIPER-TCC.sm
MOESI_AMD_Base-CorePair.sm
Notes: Example of a APU system.
Notice the shared/private caches and the single directory structure

## Slide 50: GPU VIPER Region protocol
GPU
Core
L1D
GPU
Core
L1D
GPU
Core
L1D
GPU
Core
L1D
L1I (SQC)
L2
CPU0
CPU1
L1I
L1D
L1D
L2
Directory
Memory
Controller
Memory
GPU
MOESI_AMD_Base-Region-dir.sm
GPU_VIPER-SQC.sm
GPU_VIPER-TCP.sm
GPU_VIPER-Region-TCC.sm
MOESI_AMD_Base-Region-CorePair.sm
RegionBuffer
RegionBuffer
RegionDir
MOESI_AMD_Base-RegionBuffer.sm
MOESI_AMD_Base-RegionDir.sm
Notes: Example of a APU system.
Notice the shared/private caches and the single directory structure

## Slide 51: Ruby / GPU Core interface
GPU Memory Coalescing – Critical For Performance
GPU
Core
L1D
64 “M5” Ports
one pkt per work-item request (byte address)
one RubyRequest per cache block (block-aligned address)
1 Mandatory Queue
Ruby Port
GPU Coalescer
Coalesced using lower priority events at the end of the cycle
Processed and buffered using higher priority events at the beginning of the cycle

## Slide 52: APU System: A Hierarchy of Clusters
Default Configuration
GPU
Core
L1D
GPU
Core
L1D
GPU
Core
L1D
GPU
Core
L1D
GPU I-Cache
L2
CPU0
CPU1
CPU I-Cache
L1D
L1D
L2
Directory
Memory
Controller
Memory
GPU
Cluster
CPU
Cluster
Mapping to gem5 directories:
src/mem/ruby and src/mem/protocol
src/gpu-compute
src/cpu
Main
Cluster

## Slide 53
GPU Core
L1
L2
GPU CORE
L1
NOC Router
Tiled APU System
ANOTHER GPU SUBSYSTEM CONFIGURATION
Requires minor modifications to the configuration files (src/config/ruby/GPU*.py)
Notes: Router is part of the ruby network
Networks can be simple or garnet
Remove RHS
Remove 27

## Slide 54: Outline
Topic | Presenter | Time
Background | Brad | 8:45 – 9:05
Compilation and Simulation flow | Tony | 9:05 – 9:30
GPU Core Model | Tony | 9:30 – 10:00
Break |  | 10:00 – 10:30
Ruby Memory Contributions | Brad | 10:30 – 11:00
Demo | Tony | 11:00 – 11:20
Comparisons/Limitations/Future Work | Brad | 11:20 – 11:45
Questions | Both | 11:45 – 12:00

## Slide 55: Outline
Topic | Presenter | Time
Background | Brad | 8:45 – 9:05
Compilation and Simulation flow | Tony | 9:05 – 9:30
GPU Core Model | Tony | 9:30 – 10:00
Break |  | 10:00 – 10:30
Ruby Memory Contributions | Brad | 10:30 – 11:00
Demo | Tony | 11:00 – 11:20
Comparisons/Limitations/Future Work | Brad | 11:20 – 11:45
Questions | Both | 11:45 – 12:00

## Slide 56: Comparison to other GPU Simulators
GPGPU-Sim
  Primarily focused on running Nvidia PTX instructions and CUDA applications
  Functional CPU model, oriented to model discrete GPU systems
  Wisconsin’s gem5-gpu added gem5 timing CPU models
    And a Ruby memory system protocol
  Differences from gem5-gpu:
    HSAIL instructions and OpenCL apps
    Multiple Ruby protocols
    Unified under the gem5 source control repo
Multi2Sim
  Supports multiple ISAs including AMD Southern Island’s Machine ISA
  Limited instruction support
  No transient states in coherence protocol
This is very different than the gem5 NoMALI emulated gpu device

## Slide 57: Limitations
No IOMMU
  Primitive TLB model
Not full-system
  The driver is not supporting different HSA memory segments
  There is no support for flat addressing in the emulated cl-runtime
Direct execution of HSAIL
  Does not execute finalized machine ISA kernels
  Lacks detail such as the scalar core/registers, etc.
Use of backing store for memory data
  When running applications, the data from the caches is not used
Public model has not been correlated against real hardware
No graphics functionality – compute only

## Slide 58: Obvious improvements
Detailed performance correlation
Validation of coherence protocols / memory models
  4 new coherence protocols
More programming models
  Beyond OpenCL
Other GPU ISAs

## Slide 59: APU Simulator Code Organization
gem5
src
gpu-compute
mem/
protocol
mem/
ruby
configs
cl-runtime
cl-runtime  separate tarball available: gem5.org/gpu_models
gem5 Top level directory
  --- src
  ------ gpu-compute  GPU core model
  ------ mem/protocol  APU memory model
  ------ mem/ruby  APU memory model
  --- configs
  ------ example  apu_se.py sample script
  ------ ruby  APU protocol configs

## Slide 60: Summary
Covered a very high-level overview of:
  Introduction to the gem5 APU simulator
  Mapping between APU system and gem5 APU simulator
Topics discussed
  HSA and GPU Background
  Compilation and Simulation Flow
  GPU Core modules
  GPU memory system models in Ruby
  Comparisons/Limitations/Improvements
  Code organization
Much more detail in the gem5 source code
Please contribute back to this community tool!

## Slide 61: Outline
Topic | Presenter | Time
Background | Brad | 8:45 – 9:05
Compilation and Simulation flow | Tony | 9:05 – 9:30
GPU Core Model | Tony | 9:30 – 10:00
Break |  | 10:00 – 10:30
Ruby Memory Contributions | Brad | 10:30 – 11:00
Demo | Tony | 11:00 – 11:20
Comparisons/Limitations/Future Work | Brad | 11:20 – 11:45
Questions | Both | 11:45 – 12:00

## Slide 62: Disclaimer & Attribution
The information presented in this document is for informational purposes only and may contain technical inaccuracies, omissions and typographical errors.
The information contained herein is subject to change and may be rendered inaccurate for many reasons, including but not limited to product and roadmap changes, component and motherboard version changes, new model and/or product releases, product differences between differing manufacturers, software changes, BIOS flashes, firmware upgrades, or the like. AMD assumes no obligation to update or otherwise correct or revise this information. However, AMD reserves the right to revise this information and to make changes from time to time to the content hereof without obligation of AMD to notify any person of such revisions or changes.
AMD MAKES NO REPRESENTATIONS OR WARRANTIES WITH RESPECT TO THE CONTENTS HEREOF AND ASSUMES NO RESPONSIBILITY FOR ANY INACCURACIES, ERRORS OR OMISSIONS THAT MAY APPEAR IN THIS INFORMATION.
AMD SPECIFICALLY DISCLAIMS ANY IMPLIED WARRANTIES OF MERCHANTABILITY OR FITNESS FOR ANY PARTICULAR PURPOSE. IN NO EVENT WILL AMD BE LIABLE TO ANY PERSON FOR ANY DIRECT, INDIRECT, SPECIAL OR OTHER CONSEQUENTIAL DAMAGES ARISING FROM THE USE OF ANY INFORMATION CONTAINED HEREIN, EVEN IF AMD IS EXPRESSLY ADVISED OF THE POSSIBILITY OF SUCH DAMAGES.
ATTRIBUTION
© 2015 Advanced Micro Devices, Inc. All rights reserved. AMD, the AMD Arrow logo and combinations thereof are trademarks of Advanced Micro Devices, Inc. in the United States and/or other jurisdictions. SPEC is a registered trademark of the Standard Performance Evaluation Corporation (SPEC). OpenCL is a trademark of Apple Inc. used by permission by Khronos. Other names are for informational purposes only and may be trademarks of their respective owners.